## Slide 1: CAPCOG State Water Plan Data

## Slide 2: Overview of Terminology
Existing Water Supply:
  “Maximum amount of water available from existing sources for use during drought of record conditions that is physically and legally available for use by a water user group”
Availability:
  “Maximum amount of water available from a source during the drought of record, regardless of whether the supply is physically or legally available to user groups”

## Slide 3: Overview of Terminology
Needs:
  “Projected water demands in excess of existing water supplies for a water user group or a wholesale water provider”
Water Management Strategy:
  “A plan or specific project to meet a need for additional water by a discrete water user group, which can mean increasing the total water supply or maximizing an existing supply”

## Slide 4: Overview of Terminology
Water User Group
  “Identified user or group of users for which water demands and water supplies have been identified and analyzed and plans developed to meet water needs”
  Municipal
  Manufacturing
  Irrigation
  Steam-Electric Power Generation
  Mining
  Livestock Watering

## Slide 5: Overview of Terminology
Unmet Need
  “Amount of water demand that will still exceed the water supply after applying all recommended water management strategies in a regional water plan”
Surplus
  The difference between an existing supply and demand when existing supply exceeds demand

## Slide 6: Trends 2020-2070
Chart: Acre-Feet Region-Wide
| 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Existing Supply | 740249 | 742701 | 745306 | 742518 | 737731 | 733760
Demand | 573607 | 684678 | 793741 | 896018 | 1006283 | 1130888
Needs | 34980 | 86751 | 138602 | 202034 | 311177 | 436056
Surplus with Existing Supplies | 199901 | 143294 | 88530 | 46568 | 41170 | 38332
Strategies | 262050 | 354177 | 422984 | 506274 | 593281 | 689208

## Slide 7: 2020 Supply by Type
Chart: 
| SURFACE WATER | GROUNDWATER | REUSE
Supplies (acre-feet) | 620502 | 103670 | 16077

## Slide 8: 2020 Supply by County
Chart: 
| BASTROP | BLANCO | BURNET | CALDWELL | FAYETTE | HAYS | LEE | LLANO | TRAVIS | WILLIAMSON
Supplies (acre-feet) | 36688 | 4219 | 27544 | 10563 | 56409 | 55922 | 8713 | 13588 | 423296 | 103307

## Slide 9: 2020 Demand by User Group
Chart: Demand (acre-feet)
| IRRIGATION | LIVESTOCK | MANUFACTURING | MINING | MUNICIPAL | STEAM ELECTRIC POWER
Demand (acre-feet) | 11478 | 11802 | 40303 | 22726 | 415866 | 71432

## Slide 10: 2020 Demand by County
Chart: 
| BASTROP | BLANCO | BURNET | CALDWELL | FAYETTE | HAYS | LEE | LLANO | TRAVIS | WILLIAMSON
Demand (acre-feet) | 35184 | 2656 | 18761 | 7939 | 45685 | 38017 | 8566 | 9499 | 290697 | 116603

## Slide 11: 2020 Surplus by County
Chart: 
| BASTROP | BLANCO | BURNET | CALDWELL | FAYETTE | HAYS | LEE | LLANO | TRAVIS | WILLIAMSON
Surplus (acre-feet) | 5169 | 1611 | 10041 | 2825 | 13150 | 18485 | 3327 | 4534 | 135798 | 6125

## Slide 12: 2020 Needs by User Group
Chart: Needs (acre-feet)
| IRRIGATION | LIVESTOCK | MANUFACTURING | MINING | MUNICIPAL | STEAM ELECTRIC POWER
Demand (acre-feet) | 71 | 0 | 272 | 12188 | 22449 | 0

## Slide 13: 2020 Needs by County
Chart: Needs (acre-feet)
| BASTROP | BLANCO | BURNET | CALDWELL | FAYETTE | HAYS | LEE | LLANO | TRAVIS | WILLIAMSON
Demand (acre-feet) | 4184 | 48 | 1258 | 201 | 2464 | 580 | 3180 | 445 | 3199 | 19421

## Slide 14: 2020 Strategies by County
Chart: Strategies (acre-feet)
| SURFACE WATER | GROUNDWATER | REUSE | DEMAND REDUCTION
Strategies (acre-feet) | 107569 | 28726 | 56583 | 69172

## Slide 15: 2020 Strategies by County
Chart: Strategies (acre-feet)
| BASTROP | BLANCO | BURNET | CALDWELL | FAYETTE | HAYS | LEE | LLANO | TRAVIS | WILLIAMSON
Strategies (acre-feet) | 6887 | 926 | 9608 | 2953 | 15167 | 14073 | 143 | 1725 | 148005 | 62563

## Slide 16: Strategies 2020-2070 (acre-feet)
STRATEGY TYPE | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
AQUIFER STORAGE & RECOVERY | 15,855 | 33,019 | 35,633 | 59,974 | 64,834 | 73,553
DIRECT POTABLE REUSE | 0 | 0 | 35 | 0 | 0 | 0
DROUGHT MANAGEMENT | 35,894 | 42,962 | 50,106 | 56,767 | 63,451 | 71,049
GROUNDWATER DESALINATION | 0 | 0 | 0 | 251 | 440 | 641
GROUNDWATER WELLS & OTHER | 28,726 | 37,658 | 43,255 | 50,758 | 60,805 | 68,207
INDIRECT REUSE | 39,258 | 37,749 | 42,990 | 42,874 | 46,759 | 50,312
IRRIGATION CONSERVATION | 5 | 8 | 11 | 11 | 11 | 11
MUNICIPAL CONSERVATION | 32,952 | 47,436 | 64,266 | 81,877 | 101,447 | 125,367
NEW MAJOR RESERVOIR | 13,053 | 34,421 | 47,356 | 59,636 | 88,610 | 122,418
OTHER CONSERVATION | 321 | 811 | 1,271 | 1,414 | 1,562 | 1,733
OTHER DIRECT REUSE | 17,325 | 29,057 | 42,667 | 48,189 | 56,054 | 61,636
OTHER STRATEGIES | 2,208 | 2,953 | 6,266 | 10,407 | 14,548 | 18,689
OTHER SURFACE WATER | 76,453 | 88,103 | 89,128 | 94,116 | 94,760 | 95,592
TOTAL | 262,050 | 354,177 | 422,984 | 506,274 | 593,281 | 689,208

## Slide 17: Unmet Needs 2020-2070 (acre-feet)
USER GROUP | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Bastrop County Mining | 622 | 4,356 | 4,881 | 5,644 | 6,466 | 7,377
Lee County Mining | 3,085 | 6,925 | 7,223 | 7,723 | 8,281 | 8,957
Williamson County Mining | 4,593 | 5,520 | 6,434 | 7,541 | 8,682 | 9,988
TOTAL | 8,300 | 16,801 | 18,538 | 20,908 | 23,429 | 26,322

## Slide 18: Highlights
Aggregate Regional Demand Projected to Exceed Existing Supply between 2030 and 2040
Demand reduction and reuse account for 45-48% of the strategies identified in the plan, with surface water accounting for 41-45% and groundwater accounting for 10-11%
Williamson County >50% of 2020 “needs”
Only “unmet needs:” mining in Bastrop, Lee, and Williamson Counties

## Slide 19: Thank You
Capital Area Council of Governments
www.capcog.org
Andrew Hoekzema, Director of Regional Services
ahoekzema@capcog.org
(512) 916-6043