## Slide 1: State Water Plan Supply Side Water Management Strategies in the CAPCOG Region

## Slide 2: Reminder: State Water Plan = Meeting Future Demand During a Drought of Record
Future Demand Met by Existing Supplies + Water Management Strategies (WMS)
Future conservation & reuse WMS
  Conservation & drought management = reducing amount of water used
  Reuse = turning wastewater into usable water
New supplies WMS
  Groundwater
  Surface Water
  Other strategies
Notes: Existing demand is being met by existing supplies
Future demand will be met by existing supplies, new water supplies, and conservation and reuse

## Slide 3: New Supply Water Management Strategies
Surface Water
  Aquifer Storage and Recovery
  New Major Reservoir
  Other Surface Water
Groundwater Resources​
  Aquifer Storage and Recovery
  Groundwater Desalination​
  Groundwater Wells and Other
Other Strategies
Notes: Surface Water​ is the most significant water resource on which strategies are based.
This presentation is about NEW water resources.

## Slide 4: New Supply WMS Source Definitions
Aquifer Storage and Recovery​ (ASR)
  Injecting water into an aquifer where it is stored for later use
Other Surface Water
  New minor reservoirs
  Other strategies that convey, treat, reassign, or make accessible surface water supplies to users with or without additional infrastructure
    Pipeline construction to move existing water over long distances, reassigning existing surplus water supplies, expanding water treatment plant capacity, etc.
Groundwater Wells and Other
  New wells
  Other ways to access developed groundwater supplies to users with or without additional conveyance and/or treatment infrastructure
Other Strategies
  Surface water desalination, brush control, and rainwater harvesting
Notes: GW Wells and Other
includes single wells or multiple wells, which may be part of the development of new well fields or expansions of existing well fields
maximizing the use of existing facilities by increasing production from existing groundwater wells and conveying groundwater supplies from one provider to another through a purchase

## Slide 5: Water Supply Strategies 2020-2070
Chart: Acre-Feet
| Demand Reduction and Reuse | Surface Water and Ground Water
2020 | 125755 | 136295
2030 | 158023 | 196154
2040 | 201346 | 221638
2050 | 231132 | 275142
2060 | 269284 | 323997
2070 | 310108 | 379100
Notes: Surface and ground water constitutes 52% of the water supply strategies needed in 2020 and 55% in 2070

## Slide 6: Region-Wide New Supply Strategies
Chart: Acre-Feet, 2020
| Aquifer Storage and Recovery | Groundwater Desalination | Groundwater Wells & Other | New Major Reservoir | Other Strategies | Other Surface Water
 | 15855 | 0 | 28726 | 13053 | 2208 | 76453
Notes: Other Surface Water accounts for >50% of the supply.
Groundwater Wells are the second largest supply.

## Slide 7: Region-Wide New Supply Strategies
Chart: Capital Costs by 2020
| ASR | Groundwater Wells & Other | New Major Reservoir | Other Strategies | Other Surface Water
 | 312316000 | 863644000 | 516593000 | 707263000 | 465298661
Notes: Identified costs for projects, not all costs are represented in the state water plan.
Other strategies are City of Austin Rainwater Harvesting and Regional Brush Control
Total cost for 2020 strategies: $2,865,114,661

## Slide 8: Region-Wide New Supply Strategies
Chart: Acre-Feet, 2070
| ASR | Groundwater Desalination | Groundwater Wells & Other | New Major Reservoir | Other Strategies | Other Surface Water
ASR Groundwater Desalination Groundwater Wells & Other New Major Reservoir Other Strategies Other Surface Water | 73553 | 641 | 68207 | 122418 | 18689 | 95592
Notes: New major reservoir becomes the largest supply source, with other surface water second.

## Slide 9: Region-Wide New Supply Strategies
Chart: Capital Costs, 2030-2070
| ASR | Groundwater Wells & Other | New Major Reservoir | Other Strategies | Other Surface Water
 | 28000000 | 98038000 | 711630000 | 0 | 68115674
Notes: No other strategies costs identified.
Total cost: $905,783,674
Cumulative cost for 2020-2070= $3,770,898,335

## Slide 10: New Surface Water Strategies by County
Chart: Acre-Feet
| Bastrop | Blanco | Burnet | Caldwell | Fayette | Hays | Lee | Llano | Travis | Williamson
2020 | 0 | 425 | 5298 | 2806 | 8000 | 474 | 0 | 425 | 42852 | 47289
2030 | 3452 | 425 | 12247 | 2810 | 9000 | 1021 | 0 | 475 | 66914 | 60008
2040 | 8371 | 425 | 12571 | 2827 | 11000 | 5934 | 0 | 475 | 70877 | 63759
2050 | 10778 | 425 | 12868 | 3181 | 13000 | 8024 | 0 | 475 | 102956 | 70282
2060 | 15696 | 425 | 13348 | 3652 | 15000 | 14659 | 0 | 475 | 113822 | 83531
2070 | 20619 | 425 | 13402 | 4300 | 17000 | 21916 | 0 | 475 | 127957 | 102014
Notes: New Surface Water​ is the largest WMS
Travis and Williamson will use the most acre-feet of new surface water. Blanco, Lee, and Llano do not plan to utilize new surface water.

## Slide 11: New Groundwater Strategies by County
Chart: Acre-Feet
| Bastrop | Blanco | Burnet | Caldwell | Fayette | Hays | Lee | Llano | Travis | Williamson
2020 | 3625 | 175 | 1680 | 0 | 6316 | 4571 | 0 | 200 | 500 | 11659
2030 | 3853 | 175 | 2180 | 31 | 5892 | 14222 | 0 | 200 | 1600 | 11649
2040 | 5246 | 175 | 2680 | 66 | 5404 | 17187 | 0 | 200 | 2800 | 11641
2050 | 5277 | 285 | 3480 | 316 | 4948 | 21287 | 0 | 200 | 3800 | 13560
2060 | 5850 | 285 | 4480 | 590 | 4674 | 27571 | 0 | 200 | 3800 | 15939
2070 | 5665 | 285 | 4980 | 864 | 4674 | 32293 | 0 | 200 | 3800 | 18231
Notes: Notice that the max acre-ft for groundwater is 75% less than the max surface water.
Hays and Williamson plan to utilize new groundwater supply the most.

## Slide 12: % Demand Met by New Supply Strategies by County
Chart: % of Future Demand Met by New Supply Strategies
| Bastrop | Blanco | Burnet | Caldwell | Fayette | Hays | Lee | Llano | Travis | Williamson
2020 | 0.10303 | 0.2259 | 0.37194 | 0.35345 | 0.31336 | 0.1327 | 0 | 0.065796 | 0.14913 | 0.50554
2030 | 0.15821 | 0.20527 | 0.64887 | 0.31595 | 0.32644 | 0.31664 | 0 | 0.070035 | 0.19798 | 0.50481
2040 | 0.25845 | 0.19557 | 0.59481 | 0.28732 | 0.34584 | 0.37671 | 0 | 0.070585 | 0.18482 | 0.43913
2050 | 0.26094 | 0.22597 | 0.57149 | 0.31248 | 0.33588 | 0.39477 | 0 | 0.07155 | 0.2443 | 0.41239
2060 | 0.29353 | 0.22187 | 0.56701 | 0.34315 | 0.34149 | 0.4534 | 0 | 0.070732 | 0.25003 | 0.41381
2070 | 0.29505 | 0.21975 | 0.53852 | 0.38091 | 0.34623 | 0.47123 | 0 | 0.069854 | 0.25884 | 0.43092
Notes: Remaining % = existing supplies + conservation & reuse
Lee County’s demand will be met by existing supplies and future reuse and conservation.

## Slide 13: Largest New Supply Strategies for Region
Name | Source Type | 2020 | 2070
LCRA Lane City Reservoir | Surface Water | 13,053 | 67,115
City of Austin ASR | Surface Water | 10,000 | 50,000
Brushy Creek RUA – Existing Contracts | Surface Water | 42,000 | 42,000
Little River OCR | Surface Water | 0 | 22,458
City of Austin – Lake Long Enhanced Storage | Surface Water | 22,000 | 22,000
GBRA – MBWSP – Surface Water w/ASR | Surface Water | 2,855 | 19,991
LCRA – Mid-River Basin Reservoir | Surface Water | 0 | 17,845
City of Austin – Rainwater Harvesting | Surface Water | 83 | 16,564
LCRA – Prairie Site Reservoir | Surface Water | 0 | 15,000
Carrizo Aquifer Development | Groundwater | 5,593 | 11,994
Hays/Caldwell PUA Project | Groundwater | 124 | 11,472
Georgetown WTP Expansion | Surface Water | 0 | 11,304
Vista Ridge Project | Groundwater | 9,481 | 10,700
Notes: These projects make up 77% of the new water supply strategies in 2020 and 84% of the new water supply strategies in 2070

## Slide 14: Summary
New supply strategies account for more than half of all of the acre-feet of future water supply strategies for the CAPCOG region.
“Other surface water” constitutes the largest new supply strategy in the region 2020, followed by new groundwater wells and ASR.
The region will increasingly rely on new major reservoirs, other surface water, and ASR in the future.
The capital costs greatly vary depending on the water management strategy.
The region’s future demand is heavily dependent on success of the top 13 projects.

## Slide 15: Thank you
Capital Area Council of Governments
www.capcog.org
Christiane Alepuz
calepuz@capcog.org
(512) 916-6005